## Slide 1
Minecraft 103
Computer Architecture
Oscillator
Or
Clock
Counter
Or
Memory
Decoder
Outputs
Inputs
Build-It-Yourself.com
Notes: In Minecraft 103, we will explore how a computer works.

## Slide 2
The Problem
As our civilization flourishes, there is a demand for playful and creative inventors who can build way cool machines.
Wanted:
Top notch Minecraft engineers

## Slide 3
The Mission
Be part of the Minecraft Revolution!
Build the next generation of amazing machines that will transform life as we know it. Music machines, time machines, and mind-bending games and playlands.

## Slide 4
Research
Builds that inspire!

## Slide 5
Cool Things You can do
WITH A COUNTER and Decoder
1) Control fireworks when it is 10PM at night.
2) Control a parkour game and score board.
3) Control a clock tower.
4) Control a ¾ beat in a music machine.
Build-It-Yourself.com
Notes: Trigger a fireworks display.

## Slide 6
Cool Things You can do
WITH A COUNTER and Decoder
1) Control fireworks when it is 10PM at night.
2) Control a parkour game and score board.
3) Control a clock tower.
4) Control a ¾ beat in a music machine.
Build-It-Yourself.com
Notes: Make a Parkour game with moving parts and keep track of your score.

## Slide 7
Cool Things You can do
WITH A COUNTER and decoder
1) Control fireworks when it is 10PM at night.
2) Control a parkour game and score board.
3) Control a clock tower.
4) Control a ¾ beat in a music machine.
Build-It-Yourself.com
Notes: Control a high tech clock tower

## Slide 8
Cool Things You can do
WITH A COUNTER and decoder
1) Control fireworks when it is 10PM at night.
2) Control a parkour game and score board.
3) Control a clock tower.
4) Control a ¾ beat in a music machine.
Build-It-Yourself.com
Notes: Control a ¾ beat music machine

## Slide 9
Minecraft 103
Computer Architecture
Oscillator
Or
Clock
Counter
Or
Memory
Decoder
Outputs
Inputs
Build-It-Yourself.com
What are Minecraft inputs?
What are Minecraft outputs?
What is an oscillator?
What is a counter?
What is a register?
What is memory?
Notes: In Minecraft 103, we will explore how a computer works.

## Slide 10
Computer Architecture
Oscillator
Or
Clock
Counter
Or
Memory
Decoder
Outputs
Inputs
Build-It-Yourself.com

## Slide 11
Computer Architecture
Oscillator
Or
Clock
Counter
Or
Memory
Decoder
Outputs
Inputs
Build-It-Yourself.com
A device that continuously repeats a pattern.

## Slide 12
Computer Architecture
Oscillator
Or
Clock
Counter
Or
Memory
Decoder
Outputs
Inputs
Build-It-Yourself.com
This oscillator has a 1 second period

## Slide 13
Computer Architecture
Oscillator
Or
Clock
Counter
Or
Memory
Decoder
Outputs
Inputs
Build-It-Yourself.com
Two oscillators connected.

## Slide 14
Computer Architecture
Oscillator
Or
Clock
Counter
Or
Memory
Decoder
Outputs
Inputs
Build-It-Yourself.com

## Slide 15
Computer Architecture
Oscillator
Or
Clock
Counter
Or
Memory
Decoder
Outputs
Inputs
3 stage T Flip Flop Counter
Build-It-Yourself.com

## Slide 16
Computer Architecture
Oscillator
Counter
Or
Memory
Decoder
Outputs
Inputs
Show MC number 0,1,2,3, decoders
Build-It-Yourself.com

## Slide 17
Computer Architecture
Oscillator
Or
Clock
Counter
Or
Memory
Decoder
Outputs
Inputs
Build-It-Yourself.com

## Slide 18
Minecraft 103
Mission #1
Build-It-Yourself.com
Input
Oscillator
Output
Notes: In Minecraft 103, we will explore how a computer works.

## Slide 19
Decimal vs. Binary Number System
Why do humans think in terms of 10 digits? (0-9)
Why do computers know only 2 numbers? (0-1)
Computers are dumb but very, very fast.
A computer can calculate over 1 billion additions in a second.
Build-It-Yourself.com

## Slide 20
What is Boolean Algebra?
Boolean Algebra is used to analyze and simplify the digital (logic) circuits. It uses only 0 and 1 (Binary number system)
Minecraft Redstone 102
The analog circuit needed to detect all these shades of gray is quite complex and very slow.

## Slide 21
Computer Architecture
Analog circuit Digital circuit
Build-It-Yourself.com
Input
Output

## Slide 22
Decimal | 2 | 1
0 | 0 | 0
1 | 0 | 1
2 | 1 | 0
3 | 1 | 1
Decimal | 4 | 2 | 1
0 | 0 | 0 | 0
1 | 0 | 0 | 1
2 | 0 | 1 | 0
3 | 0 | 1 | 1
4 | 1 | 0 | 0
5 | 1 | 0 | 1
6 | 1 | 1 | 0
7 | 1 | 1 | 1
Decimal vs. Binary Number System
Boolean Algebra is used to analyze and simplify digital (logic) circuits.
It uses only digits 0 and 1. (binary number system)

## Slide 23
What is Boolean Algebra?
Boolean Algebra is used to analyze and simplify the digital (logic) circuits. It uses only 0 and 1 (Binary number system)
Challenge: Fill in the o’s and 1’s
Minecraft Redstone 102
Decimal | 2 | 1
0 |  | 
1 |  | 
2 |  | 
3 |  | 
Decimal | 4 | 2 | 1
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 

## Slide 24
Boolean Algebra is used to analyze and simplify digital (logic) circuits.
It uses only digits 0 and 1. (binary number system)
10’s | Units | 8 | 4 | 2 | 1
0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1
0 | 2 | 0 | 0 | 1 | 0
0 | 3 | 0 | 0 | 1 | 1
0 | 8 | 1 | 0 | 0 | 0
1 | 2 | 1 | 1 | 0 | 0
1 | 5 | 1 | 1 | 1 | 1
Decimal
Binary
Decimal vs. Binary Number System

## Slide 25
Computer Counter + Decoder
Build-It-Yourself.com
0 | 1 | 2 | 3
0 | 1 | 0 | 1
0 | 0 | 1 | 1
FF1
FF2
State Table or Truth Table
Count
1 = True = On
0 = False = Off

## Slide 26
Computer Counter + Decoder
Build-It-Yourself.com
What is an oscillator?
Clock
Or Oscillator
Tic
0
Toc
1
Tic
0
Toc
1
Tic
0
Toc
1

## Slide 27
Computer Counter + Decoder
Build-It-Yourself.com
What is a Flip Flop?
When you trigger a Flip Flop it changes state
Input
Pulse or Oscillator
T-Flip Flop
Trigger
Output
0 or 1
Tic
0
Toc
1
Tic
0
Toc
1
Tic
0
Toc
1
Tic
0
Toc
1
Tic
0
Toc
1
Tic
0
Toc
1
Tic
0
Toc
1
T-Flip Flop
JK-Flip Flop
SR-Flip Flop
D-Flip Flop (protect against S=0 and R=0)

## Slide 28
Computer Counter + Decoder
Build-It-Yourself.com
0 | 1 | 2 | 3
0 | 1 | 0 | 1
0 | 0 | 1 | 1
FF1
FF2
State Table or Truth Table
Count
1 = True = On
0 = False = Off
0
1
2
3
clock
FF1
FF2
0
1
2
3
Count
0
0
0
1
1
0
1
1
Timing Diagram

## Slide 29
Computer Counter + Decoder
Build-It-Yourself.com
FF1
FF2
c
0 | 1 | 2 | 3
0 | 1 | 0 | 1
0 | 0 | 1 | 1
FF1
FF2
State Table or Truth Table
Count
1 = True = On
0 = False = Off
0
1
2
3
clock
FF1
FF2
0
1
2
3
Count
0
0
0
1
1
0
1
1
Timing Diagram
Trigger or T Flip Flop

## Slide 30
Computer Counter + Decoder
Build-It-Yourself.com
FF1
FF2
c
0 | 1 | 2 | 3
0 | 1 | 0 | 1
0 | 0 | 1 | 1
FF1
FF2
State Table or Truth Table
Count
1 = True = On
0 = False = Off
0
1
2
3
clock
FF1
FF2
0
1
2
3
Count
0
0
0
1
1
0
1
1
Timing Diagram
Trigger or T Flip Flop

## Slide 31
Computer Counter + Decoder
Build-It-Yourself.com
FF1
FF2
c
0 | 1 | 2 | 3
0 | 1 | 0 | 1
0 | 0 | 1 | 1
FF1
FF2
State Table or Truth Table
Count
1 = True = On
0 = False = Off
0
1
2
3
clock
FF1
FF2
0
1
2
3
Count
0
0
0
1
1
0
1
1
Timing Diagram
Trigger or T Flip Flop

## Slide 32
Computer Counter + Decoder
Build-It-Yourself.com
FF1
FF2
c
0 | 1 | 2 | 3
0 | 1 | 0 | 1
0 | 0 | 1 | 1
FF1
FF2
State Table or Truth Table
Count
1 = True = On
0 = False = Off
0
1
2
3
clock
FF1
FF2
0
1
2
3
Count
0
0
0
1
1
0
1
1
Timing Diagram
Trigger or T Flip Flop

## Slide 33
Minecraft 103
Mission #2
Build-It-Yourself.com
Build an 8 state counter
Notes: In Minecraft 103, we will explore how a computer works.

## Slide 34
Computer Counter + Decoder
Build-It-Yourself.com
T
Q1
FF1
T
Q2
FF2
FF2
FF2’
FF1
FF1’
C`
0
1
2
3
0
1
2
3
clock
FF1
FF2
0
1
2
3
clock
Show MC
Oscillator,
flip flops
and decoder

## Slide 35
Computer Counter + Decoder
Build-It-Yourself.com
T
Q1
FF1
T
Q2
FF2
FF2
FF2’
FF1
FF1’
C`
0
1
2
3
0
1
2
3
clock
FF1
FF2
0
1
2
3
Show MC
Oscillator,
flip flops
and decoder

## Slide 36
Computer Counter + Decoder
Build-It-Yourself.com
T
Q1
FF1
T
Q2
FF2
FF2
FF2’
FF1
FF1’
C`
0
1
2
3
0
1
2
3
clock
FF1
FF2
0
1
2
3
clock
Show MC
Oscillator,
flip flops
and decoder

## Slide 37
Computer Counter + Decoder
Build-It-Yourself.com
T
Q1
FF1
T
Q2
FF2
FF2
FF2’
FF1
FF1’
C`
0
1
2
3
0
1
2
3
clock
FF1
FF2
0
1
2
3
clock
Show MC
Oscillator,
flip flops
and decoder

## Slide 38
Computer Counter + Decoder
Build-It-Yourself.com
T
Q1
FF1
T
Q2
FF2
FF2
FF2’
FF1
FF1’
C`
0
1
2
3
0
1
2
3
clock
FF1
FF2
0
1
2
3
clock

## Slide 39
Computer Counter + Decoder
Build-It-Yourself.com
T
Q1
FF1
T
Q2
FF2
FF2
FF2’
FF1
FF1’
C`
0
1
2
3
0
1
2
3
clock
FF1
FF2
0
1
2
3
clock

## Slide 40
Computer Counter + Decoder
Build-It-Yourself.com
T
Q1
FF1
T
Q2
FF2
FF2
FF2’
FF1
FF1’
C`
0
1
2
3
0
1
2
3
clock
FF1
FF2
0
1
2
3
clock

## Slide 41
Computer Counter + Decoder
Build-It-Yourself.com
T
Q1
FF1
T
Q2
FF2
FF2
FF2’
FF1
FF1’
C`
0
1
2
3
0
1
2
3
clock
FF1
FF2
0
1
2
3
clock

## Slide 42
Minecraft 103
Mission #3
Build-It-Yourself.com
Build decoders that produce a pulse for states 2 and 5
Notes: In Minecraft 103, we will explore how a computer works.

## Slide 43
Latches, Registers, Memory
Build-It-Yourself.com
0
1
2
3
clock
FF1
FF2
0
1
2
3
Document 3 types of Flip Flops
T
Set / Reset
JK

## Slide 44
Minecraft 103
Mission #4
Build-It-Yourself.com
Build latches or registers that turn on at state 2 and turn off at state 5
Notes: In Minecraft 103, we will explore how a computer works.

## Slide 45
Minecraft 103
Missions #5, #6, #7, #8
Build-It-Yourself.com
Build
Parkour game,
clock tower,
music machine or
fire works display
Notes: In Minecraft 103, we will explore how a computer works.

## Slide 46
Minecraft 103
Concepts you should be able to explain
Build-It-Yourself.com
5 components in computer architecture.
  Oscillator
  Input devices
  Output devices
  Counters, Memory and Registers
  Decoders
Timing diagrams
Binary vs. Decimal number system
Boolean Algebra for AND, OR, and NOT
Notes: In Minecraft 103, we will explore how a computer works.